VoIP

Addressing QoS Beyond the

Provider Network

This White Paper explores the issue of voice

quality in VoIP networking and current status

of QoS technologies and implementations in

today’s  IP  networks.  We  discuss  the  QoS

mechanisms SmartNode™ employs to ensure the best-possible voice quality over the network-

access link.

Copyright

Copyright © 2006, Patton Electronics Company. All rights reserved.

Printed in the USA.

Introduction

Today’s Internet does far more then email and file transfers. Initially designed for non-real-time (NRT) data applications, the Internet has matured far beyond these tasks. In addition to web browsing, online imaging, and chat rooms, we now expect the Internet to deliver such real-time  (RT)  media  as  streaming  music,  video,  and Internet phone calls directly to our homes and offices.

Presently,  Voice-over-Internet  Protocol  (VoIP)  is  all  the buzz—but it’s more than just talk. VoIP technology has matured. Not only is it  the  latest hot new Internet appli- cation. Today,  VoIP  has emerged as a reliable technol- ogy  that  is  commercially  viable,  competing  (and  win- ning) against  traditional phone services in business and consumer-class  markets.

As a real-time application, VoIP—also known as packet voice,   packet   telephony,   or   IP   telephony—places increased demands on the evolving Internet. VoIP users expect  the  Internet  to  deliver  toll-quality  voice  with  the same clarity as the traditional Public Switched Telephone Network   (PSTN).  To   meet   those   expectations,   the Internet connection must be more than merely  reliable, it must be time-sensitive. Each and every voice packet must be delivered without significant delay and with consistent time intervals between packets.

Advanced Quality of Service (QoS) technology is the key

to achieving voice quality that measures up to today’s high standards. With SmartNode and Patton’s advanced QoS, toll-quality voice  on  every call is the benchmark.

Quality  of  Service  (QoS)—In  a  successful  VoIP deployment,  the  perceived  voice  quality  of  VoIP  calls must satisfy user expectations. Specifically, voice quali-

ty in the VoIP system must compare favorably with that

of a traditional phone call. To ensure VoIP users hear

the  best  possible  voice  quality,  Patton’s  SmartNode employs a unique combination of varied QoS mecha- nisms.  Network  administrators  can  tune  SmartNode’s QoS for optimal performance in a broad range of net- works giving packet voice the clarity and sound quali-

ty we expect on every call.

QoS and voice quality

From  a  technical  perspective  good  voice  quality involves minimizing delays and interruptions (“blips”) in the  communication  stream.  For  voice  communications over an IP network, packet delays and losses in the VoIP network  must  be  reduced  to  the  levels  of  established benchmarks. To achieve a level of perceived voice quali-

ty  that  most  users  find  acceptable,  end-to-end  packet delay must be reduced to a target of 120ms or less. In most  IP  networks  some  degree  of  packet  loss  may  be inevitable. However, for a successful VoIP deployment, we must reduce packet loss to well below 1%. For Fax-over-

IP connections, the packet-loss target is especially critical.

Packet loss and packet delay may accumulate at multiple  locations  within  the  IP  network.  Every  router, switch and transmission line is a potential culprit for har- boring these enemies of voice quality. Technology stan- dards such as TOS or DiffServ are designed to achieve the goal of establishing QoS in each and every node, thus enforcing QoS mechanisms throughout the network from end to end. (These standards will be discussed later

in this paper.) The reality today, however, is an Internet that  does  not  differentiate  between  real-time  (RT)  and non-real-time (NRT) packets. As a result, VoIP networks require alternate methods for ensuring voice quality.

Addressing QoS at the edge of

the network

In VoIP systems that traverse the Internet, the bottleneck  typically  occurs  at  the  access  link—the  low- bandwidth connection between the high-speed Internet- backbone (WAN) and the user network (LAN). Both net- works  typically  run  at  100  Mbps  or  above.  A  typical access link may easily run about 200 times slower than the LAN residing in the home or office (say, 512 kbps for example). Congestion, queuing delay, and queue over- flows  (resulting  in  dropped  packets)  are  most  likely  to occur on this link. Depending on access-link bandwidth, packet size and burst size (the number of packets arriv- ing at once), queuing delay can be especially significant.

In a typical installation, a single access link serves both voice and data traffic, so special measures must be  employed  to  ensure  good  voice  quality.  Consider the case of a 256 kbps access link from the Internet’s edge  router  to  the  user’s  LAN.  Suppose  the  Internet’s transmit  queue  contains  five  1500-byte  data  packets, followed by one time-sensitive voice packet. It will take roughly  270  ms  to  send  those  data  packets  over  the

256  kbps  link.  When  the  voice  packet  follows,  it arrives with a delay longer than 120 ms (our target),

resulting in degraded voice quality.

Introducing class-of-service in the packet layer

addresses  queuing  delay  by  ensuring  voice  packets receive  priority  treatment—in  much  the  same way that separate queues at airport check-in counters ensure pri- ority service to first-class customers. By creating separate queues for Real-Time and Non-Real-Time traffic, we can assign higher priority to the RT queue and serve that traf- fic with higher priority.

Upstream and downstream traffic present different problems, and are best addressed by different Quality of Service (QoS) mechanisms. Upstream traffic flows from the  (home  or  office)  user  to  the  Internet,  while  down- stream traffic flows from the Internet to the user.

Implementing QoS in the upstream direction is relatively  easy.  SmartNode™  ensures  that  outbound voice packets get served before other packet types to prevent  the  Internet  access  link  (the  bottleneck)  from becoming  overloaded.  SmartNode  also  provides  tun- ing mechanisms for additional parameters like packet segmentation  and  overhead  optimization,  so  network administrators can further fine-tune the upstream trans- mission for optimum voice quality.

Implementing QoS in the downstream direc- tion  is  more  complex.  Typically,  customer-premise equipment  (CPE)  at  user  locations  exerts  no  control

Figure 1. Internet Access

Figure 2. The Problem of Downstream Traffic

over  incoming  traffic.  For  traffic  flowing  downstream

from the Internet, the access router cannot control the volume nor the sending users. In addition, local users sharing the LAN with you can initiate file transfers or download their email at their convenience. The servers handling  these  requests  may  be  located  anyplace. Since  the  downstream  rate  normally  cannot  be  con- trolled,  the  ISP’s  edge  router  commonly  responds  to overloading by discarding VoIP packets with the same probability as any other packet type. These factors, or

a combination of them, may degrade voice quality to

a degree that users find objectionable. Data traffic, on the other hand, can be retransmitted so the impact on the user experience is simpler slower service response.

To  resolve  the  problem  of  degraded  voice quality for incoming traffic, Patton has devised a lead- ing-edge	technology	for	SmartNode™	called DownStreamQoS™.  Within  the  SmartNode  deployed at the customer premise, DownStreamQoS dynamically creates a virtual bottleneck against the incoming pack-

et  stream.  This  bottleneck  can  throttle  back  Non-Real-

Time traffic, preventing the edge router from blocking

or impeding voice traffic, to ensure voice packets are transmitted	freely	downstream.	DownStreamQoS employs flow-control mechanisms within the TCP stan- dard to create the bottleneck. Because 80% of Internet traffic is transported via TCP, DownStreamQoS is espe- cially effective. The dynamic bottleneck adjusts to vary- ing traffic patterns. So whenever there are no VoIP calls

in progress, the full downstream bandwidth is available for incoming data such as file downloads.

Technology standards for QoS When  implementing  QoS  to  ensure  good  voice quality, VoIP networks may employ a selection of mech- anisms from a variety of standard communications pro- tocols. Such mechanisms may include:

•	Tag or Label within the Packet or Frame

•	Traffic (QoS) Classes

•	Traffic (QoS) Conditioning or Packet treatment

Figure 3. SmartNode™ DownStreamQoS™

The  table  below  summarizes  the  standard  protocol

mechanisms Patton has employed in our unique imple- mentation of QoS for SmartNode VoIP solutions.

A key point to remember about any QoS-related standard is the following: a standard is only as effec- tive  as  its  specific  implementation  in  a  specific  net- work  in  the  real  world.  For  example,  almost  every router in the world claims to support TOS labeled IP packets. “So why,” we want to ask, “is the Internet still

a best-effort network? Why has the Internet not imple- mented QoS?” The answer lies in the additional com-

plexity of administering a network that delivers QoS.

A network operator who wants to offer different serv-

ice classes must do all of the following:

•	Provide Service Level Agreements (SLAs) for the service classes offered (e.g. throughput guarantees or maximum delay values)

•	Bill separate service classes individually

•	Ensure that service classes are not fraudulently misused

•	Dimension the network in a way so that SLAs for each service class can be met, even in fallback and redundancy scenarios

Standard

IEEE 802.1pQ

Layer

2 (Ethernet)

QoS Label

3 bits in Ethernet Header

Description

Extended Ethernet frame for VLAN and QoS.

Defines eight Priority Classes.

MPLS	2 (ATM, FR or Shim Label on IP)	Not applicable	Label switching protocol for core routers.

Can be used for traffic engineering, VPN

and QoS differentiation.

TOS/Precedence	3 (IP)	1 octet in IP Header	Defines three traffic characteristics:  low delay, high throughput, high reliability

DiffServ	3 (IP)	Same octet in IP Header as TOS	Defines a 6-bit field for service classes and

a number of Per-Hop Behaviors (PHB)

on how to treat packets

6

Administering a QoS network is much more com-

plex  than  ensuring  reliable  connectivity  in  a  best-effort network. This complexity is why networks supporting dif- ferent  service  classes  have  not  appeared  until  quite recently, and only a limited scale, and only from single operators. Considering the content of our discussion, one can begin to grasp the complexity of implementing QoS end-to-end across the boundaries of multiple networks.

Conclusion

The Internet Engineering Task Force (IETF) and the networking industry have defined a number of tech- nology standards and methods for offering levels of IP- network service that exceed the typical best-effort serv- ice  levels  currently  available.  Yet  the  reality  today  is that IP Networks—and the Internet in particular—con- tinue to lag behind in implementing these existing tech- nologies  in  order  to  deliver  QoS  to  subscribers.  The reason for the delay lies in the substantial complexity involved in administrating a QoS network.

SmartNode  has  implemented  QoS  mecha- nisms  that  significantly  improve  service  quality  for voice and data in a crucial section of the network— the subscriber access link. Further, SmartNode’s QoS mechanisms  operate  with  complete  independence from  the  Internet  or  wide  area  network.  Finally, SmartNode  is  flexibly  designed  for  future  adapta- tion,  ready  and  able  to  support  leading  QoS  tech- nology  standards  as  network  providers  begin  to deploy them.

Today’s   enterprises,   carriers   and   service-

providers  are  eager  to  realize  the  cost-savings  and flexibility  of  VoIP.  Patton’s  SmartNode™  family  of  VoIP solutions offers a complete line of VoIP Gateways and Broadband Internet Access Routers that deliver those cost and  flexibility  benefits  now,  while  offering  a  smooth migration path to tomorrow’s fully-converged voice-data networks. Scaling from dual-port analog gateways up to Quad-PRI   digital   Gateway-Routers,   all   SmartNode™ models combine standards-based signaling (SIP, H.323 and  MGCP/IUA)  with  advanced  Patton’s  feature-rich SessionRouter™  software  to  deliver  robust  Telephony- over-IP  with  industry-leading  voice  quality.  SmartNode VoIP solutions integrate seamlessly with legacy communi- cations infrastructures to deliver end-to-end voice servic- es   over   any   IP   network.   SmartNode™/SmartLink™ VoIP…more than just talk!

Key  SmartNode  features  to  make  your  VoIP  project

a success:

•	Standards Compliance—Protecting your investment in VoIP, SmartNode implements key industry standards for proven interoperability with third-party equipment and networks.

•	Advanced Call Routing—SmartNode’s flexible SessionRouter software seamlessly integrates VoIP with existing telephony systems and numbering plans.

•	Feature Transparency—SmartNode forwards PBX and PSTN features transparently to the user, preserving the benefits of advanced calling fea- tures in both traditional telephony and digital packet-voice networks.

7

Product Line

Series

Description

S-ATA

S-DTA SN41XX SN402X SN455X SN452X SN48XX SN463X SN465X SN1200/1400

SN2350

SN2300

SN4900

SN2450

SN2400

Residential Smart Analog Telephone Adapter

Residential Smart Digital (BRI) Telephone Adapter

Multi-Port Analog VoIP Gateway

Analog VoIP SOHO Router ISDN BRI VoIP SOHO Router Multi-Port Analog VoIP IAD

Multi-Port Analog IAD with Integrated WAN Access

Multi-Port ISDN VoIP IAD

Multi-Port ISDN VoIP IAD with Integrated WAN Access

ISDN BRI VoIP Gateway Modular VoIP Gateways Modular VoIP Routers IpChannel Bank

4-Slot Modular VoIP Gateways

4-Slot Modular VoIP Routers

Low Cost Analog

& ISDN Adapters

•   Low Cost simplified VoIP Gateways

•   Plug and Go Feature Set

•   Two Models for both Analog and

ISDN Phones

•   Single and Multiline with full

FAX support

Branch Office Routers

with VoIP

•   SOHO VoIP with seamless connection to enterprise voice and fax

•   Analog or digital options for one or two lines

•   Network compatibility features allowing use virtually any IP service network with VPN, QoS, and Firewall features

•   Single box LAN/WAN integration

Mutiport Analog & ISDN

with integrated WAN

•   Small enterprise; branch/satellite office

•   Voice extension and PBX voice and data

networking; any-access-to-any-network

•   PSTN access with FXS and FXO and

FXS/FXO combinations; or ISDN BRI So

•   Complete LAN/WAN routing with QoS,

VPN, and network integration for a sin-

gle-box solution

•   Integrated WAN options for full routed

connections with PPP/Frame Relay

IpChannel Bank

•   Analog trunking VoIP

•   Multiport analog connections for call

centers

•   Expansion slot for integrated WAN

uplinks using PPP/Frame Relay

•   Reliability with redundant power and

redundant Ethernet

•   Low to high density (from 12 to

32) analog ports

# Text boxes

Large Enterprises

Medium Enterprises

Carrier