SIP Security and

the IMS Core

SIP SECURITY AND THE IMS CORE

uch has been written about the security of SIP-

based networks and security of Voice over IP

in  general,  but  ultimately  good  security  is  a complete architecture, not a single product or protocol. The advent of Fixed/Mobile Convergence and IMS has created   some   widely   accepted   standards   and   has equally   highlighted   architectural   differences   in   the converging  networks.  Whilst  the  overall  objective  of providing a flexible, secure network and secure services

is   common,   the   implementation   details   differ   from network to network.

Even  within  the  standards  themselves  there  is  sometimes  an assumption  of  trust  which  may  not  in  reality  exist.	For example,  the  IMS  definition  within  TISPAN  assumes  that  the signalling  elements  are  able  to  handle  excessive  signalling rates  and  badly  formed  signalling  messages.  In  reality  these elements are designed to process sessions, handling attacks at the same time may not be the best use of the equipment.  In a data-centric network we would expect to see servers ringed by Firewalls  and  Intrusion  Detection  and  Prevention  systems,  so why would we build a media-centric network any other way?

Fixed/Mobile Differences

The  networks  that  support  mobile  services  have  developed their  own  security  and  authentication  mechanisms  that  reside primarily in the radio access part of the network. This means that when 3GPP developed their IMS specification there was no need to be overly concerned with those issues.   The IMS can assume that the subscriber that is registering has already been authenticated and that the only thing to deal with now is the policies that apply to the caller.  In the case of a fixed line service   there   is   no   guarantee   that   the   user   will   be authenticated	against	a	USIM	(Universal	Subscriber Information  Module),  thus  authentication  must  rely  on  other, potentially less secure techniques.

This ability to connect almost any hardware or software device opens  the  door  to  other  potential  problems  in  the  fixed  line network  –  that  of  device  malfunction  and  malicious  attack. The  mobile  radio  access  network  is  a  far  more  controlled

environment,  with  each  device  having  a  security  association

with  the  network,  meaning  that  any  abuse  can  be  tracked

back to a particular device. Another consideration is that there

is currently a marked difference in the bandwidth available in fixed and mobile networks, thus the fixed line network offers a potentially  larger  pipe  to  deliver  disruptive  traffic.  Fixed  line networks  will  support  a  large  population  of  PC  based  soft- clients, these require minimal testing and therefore the potential for the presence of badly behaved device is much greater, it also means that a familiar environment is available for creating malicious software.

ETSI's TISPAN architecture takes the 3GPP IMS definition and expands  it  to  include  addition  elements  that  help  to  address some of these concerns.  The most noticeable difference is that the 3GPP definition deals only with the signalling path whilst the  TISPAN  definition  includes  elements  that  manage  the media path, the BGFs – Border Gateway Functions.   There is also	a	formalised	Border	Control	Function	between interconnected networks – the I-BCF.

The  3GPP  IMS  security  architecture  is  based  around  IPsec, which works well in the 3G environment which does not have NAT  devices.  Most  NAT  devices  translate  port  numbers  as well as IP addresses, which due to the way IPsec encodes the packets means that NAPT devices will prevent end-to-end use of IPsec.

However,   in   TISPAN   with   client   devices   typically   being connected through broadband access networks NAPT devices are   virtually   guaranteed.   Thus,   TISPAN   encryption   and authentication must take another route. RFC3261 specifies TLS as  the  secure  transport  mechanism  for  use  with  SIP,  and  this was considered by TISPAN, however, the selected encryption method  is  UDP  encapsulation  of  IPsec.  This  eliminates  the problems encountered when using IPsec across NAPT devices. IPsec,   NAT   traversal   and   TISPAN's   selection   of   UDP encapsulated  IPsec  are  examined  the  White  Paper  "IPsec  in VoIP Networks".

IMS as the Heart of the Network

The role of an IMS core is to enable service providers to roll out new services rapidly and deliver them to any device over any network. It is the glue that sits between the service layer

and the network layer. Whilst these elements can be expected

to  provide  some  level  of  resilience  to  attacks,  pragmatic

service  providers  are  looking  to  create  a  protected  zone  in which these highly valuable assets can be located.

So  we  are  in  effect  talking  about  creating  a  DMZ  for  the signalling through the use of 'signalling firewalls'.   The job of the  signalling  firewall  is  to  protect  the  core  elements  from accidental  overload,  malicious  attack,  malformed  signalling messages and irrelevant protocols.

Protect the core with signalling firewalls

IP Network

SIP  signalling  traffic  must  also  be  viewed  with  considerable

suspicion, malformed SIP messages should be discarded and not  passed  through  to  the  IMS  core  elements.   Resistance  to this type of attack can be determined by testing against suites such  at  the  IETF  SIP  Torture  test  developed  through  the  SIPiT Events or the PROTOS Test-Suite, developed by the University of Oulu.

Requirement 2: Must prevent propagation of attacks

This  is  the  logical  extension  of  the  first  requirement.  The signalling firewall must identify and discards malicious traffic in order  to  protect  the  core.  Many  protocols  can  simply  be discarded,  as  described  in  Requirement  1  above,  as  they have no relevance to the SIP proxies. Thus the IMS  elements

are  effectively  protected  from  both  transport  and  application

Access

Network

Untrusted

Zone

IMS

Trusted

Zone

Peer

Network

Untrusted

Zone

layer attacks.

Requirement  3:  Must  preserve  an  operational  service through pacing

Now that the basics are in place we must turn our attention to the applications themselves.  The rate of SIP signalling can be the cause of problems for the Softswitch and not just through

malicious  intent,  for  example,  following  the  hurricanes  in

Providing   protection   for   the   core   requires   more   than   a

conventional firewall, it requires a firewall that can understand SIP  signalling.	This  requires  a  resilient  hardware  based solution   capable   of   rejecting   any   unwanted   traffic   whilst admitting  legitimate  traffic  at  a  rate  which  can  be  supported by  the  core  elements.  Not  a  trivial  task  -  lets  look  at  the requirements one by one.

Requirement 1: Must stand up under attack

A  basic  requirement  of  any  signalling  firewall  is  that  it  must remain operational under all attack conditions.  Before we get carried away with all of the exotic and innovative application layer  attacks,  the  basics  must  be  in  place.    The  TCP  SYN flood,  for  example,  is  one  of  the  oldest  attacks  around  and probably  one  of  the  most  common  exploits  used  to  cause resource  starvation  in  vulnerable  targets.  The  IMS  core  may not  need  to  even  respond  to  any  TCP  traffic  if  the  SIP signalling is carrier using UDP, thus TCP traffic can be rejected at  the  perimeter  of  the  IMS.   Similarly  logic  exploits  like  the Ping of death, should simply be blocked by the firewall at the IMS  perimeter.	A  minimum  requirement  for  the  signalling firewall is that is should stand up to vulnerability tests such as

ISIC - IP Stack Integrity Checker and Nessus.

Florida  when  the  power  was  restored,  this  caused  all  the  IP phones  to  register  at  the  same  time.	This  resulted  in  the service  failing  due  to  the  rate  of  registrations.	In  these situations the core elements must be protected by pacing both registrations and call attempts.   The signalling firewall should deliver the registrations and call invitations to the Softswitch at

a rate that it can sustain.

Requirement   4:   Must   preserve   network   anonymity through topology hiding

Topology hiding features prominently in most service providers' requirements.  As  the  SIP  signalling  passes  through  various servers  on route  to  its  destination,  the  SIP  messages  acquires information  about  where  the  message  came  from  and  what devices  it passed  through.   Since  global  networks  are  made up of a mesh of service provider networks this information gets passed  from  network  to  network.   It  is  therefore  important  to strip  all  this  information  from  the  signalling  prior  to  it  being passed  from  one  network  to  another.  This  prevents  internal network  addresses  and  client  address  details  from  being propagated.   This  benefits  the  service  provider  by  effectively shielding both network and subscriber from prying eyes.

Requirement   5:   Must   preserve   service   quality   and

protect revenue through media policing

This  requirement  is  present  to  counter  some  of  the  innovative ploys  to steal services. When  SIP  establishes  a  call it uses a server  to  locate  and  communicate  with  the  destination,  once the   addresses   of   the   source   and   destination   have   been exchanged  there  is  no  reason  why  the  two  parties  cannot communicate  directly  –  without  the  intervention  of  the  server. Thus, a party  can request a  voice call which,  once establish can be renegotiated as a video call without the knowledge of the  SIP  servers  from  which  the  billing  may  be  derived.   The service provider is unaware of the addition bandwidth being used. This results in loss of revenue and potential degradation of service quality for other users.

To  prevent  this  service  theft  it  is  necessary  to  link  the  media path  with  the  signalling  path.  This  is  carried  out  by  session border  controllers,  or  in  the  case  of  a  TISPAN  IMS,  by  a combination   of   the   P-CSCF   and   A-BGF   managing   the signalling and media respectively.   The signalling and media elements   exchange   information   to   ensure   that   the   media remains  within  the  requested  limits,  any  deviation  from  the requested bandwidth can be blocked.

A  key  benefit  of  this  process  is  to  preserve  the  Quality  of Service  of  calls,  particularly  within  the  access  networks,  by preventing over-booking of the network resources.

The Survivable Core

With all of the above requirements satisfied we have helped to   create   a   survivable   core.   Through   a   combination   of firewalling,   signal   pacing   and   traffic   management,   the valuable  assets  that  make  up  the  IMS  core  can  get  on  with doing their job: providing any service to any device over any network.

Is  the  signalling  firewall  a  logical  component  or  a  physical device?  The  answer  is  actually  both.	There  are  several functions within the 3GPP and TISPAN IMS definitions that can be  considered  to  be  border  devices.  The  P-CSCF  is  the  first point of contact for registration and routing of new calls and is therefore   a   suitable   device   in   which   to   implement   the signalling  firewall.  The  I-CSCF  provides  topology  hiding  for the  interconnect  point.  Within  TISPAN,  the  BCF  and  BGF functions  define  signalling  and  media  borders.	All  these functions may be extended to include the requirements defined

above  as  part  of  a  fully  integrated  solution.    Equally,  it  is

possible to treat the whole IMS as a target and implement the

signalling and media protection externally.

What next? SPIT – Detection and Deflection SPAM  over  Internet  Telephony,  or  SPIT  as  it  so  colourfully known, is being touted as the next e-plague to descend upon

us. This is the voice equivalent  of email SPAM, i.e. machine

driven mass dialling to subscribers to deliver junk voice mail. So how can we deal with this? The answer may lie in a two layered  defence  of  detection  and  deflection.    Many  of  the best  SPAM  filters  around  today  are  in  fact  great  learning machines,  they  constantly  learn  what  is  SPAM  and  what  is not, they build black lists of known sources and can achieve high rates of successful blocking.  However, SPAM is non-real- time,  in  order  to  apply  this  technology  to  SPIT  the  detection engine must employ pattern recognition on calls to determine

a  potential  source,  this  can  be  carried  out  non-intrusively  in near-real-time, the results written to a policy database which is accessed by the signalling firewall which deflects or blocks the signalling and prevents the call from being established.

Conclusion

IMS offers the potential to deliver a great range of innovative services to a range of different networks.   In doing so it offers an  attractive  target  for  disruption.  The  IMS  core  must  be protected  through  the  use  of  an  effective  security  architecture either  intrinsically  as  part  of  the  perimeter  of  the  IMS  e.g.  a hardened   P-CSCF   acting   as   a   signalling   firewall,   or extrinsically by using signalling firewalls to create a DMZ for the core elements.

Newport Networks 1460 provides the carrier class hardware platform required for these duties, either as a P-CSCF itself, or as  a  signalling  firewall  protecting  a  third  party  P-CSCF.  The

1460 can also offer separated signalling and media elements capable of offering full topology hiding and media policing.

Guaranteeing continuity of service is an impetrative for service providers  deploying  IMS  cores.	The  survivable  core  also forms  the  cornerstone  of  delivering  reliable  Emergency  Call Handling  and  key  worker  prioritisation  –  this  is  discussed  in more  detail  in  Newport  Networks  Emergency  Call  Handling White Paper. ■

Glossary

A-BGF	Access Border Gateway Function

BCF	Border Control Function

BGF	Border Gateway Function

I-BCF	Interconnect Border Control Function

I-BGF	Interconnect Border Gateway Function

I-CSCF	Interrogating-Call Session Control Function

IMS	IP Multimedia Subsystem

IPsec	IP Security Protocol

NAPT	Network Port and Address Translation

NAT	Network Address Translation

P-CSCF   Proxy-Call Session Control Function

SIP	Session Initiation Protocol

SPIT	SPAM over Internet Telephony TCP	Transmission Control Protocol TLS	Transport Layer Security

TISPAN   Telecoms & Internet converged Services & Protocols

for Advanced Networks

UDP	User Datagram Protocol

USIM	Universal Subscriber Information Module

Other White Papers

You may find the following White Papers of interest: IPsec in VoIP Networks

SIP, Security and Session Controllers

Lawful Interception Overview

These and other papers can be found at:

http://www.newport-networks.com/whitepapers

The Newport Networks’ logo is a registered trademark of Newport Networks Ltd.  MediaProxy™ and SignallingProxy™ are trademarks of Newport Networks Ltd.  ©2006 Newport Networks Limited.  All rights reserved. Whilst every effort has

been made to ensure that the information included in this publication is accurate at the time of going to press, Newport Networks Ltd assumes no responsibility for the accuracy of the information.   Newport Networks Ltd reserves the right to change their specifications at any time without prior notice.   Some features described in this document may be planned for future releases and may not be available in the current product.   Newport Networks Ltd reserves the right to modify its product development schedule without notice and does not guarantee that any feature or product mentioned in this document will be produced or produced in the form described.

91-0088-01-0001-A

# Text boxes

M

n