Secure,	Multi-lateral	Peering

with	AsteriskTM V1.2

22 November 2005

Contents

Multi-lateral Peering: Why ............................................................................................................. 1

Current Deployments .................................................................................................................. 1

Distributed Architecture.......................................................................................................... 1

Centralized Architecture ......................................................................................................... 2

Multi-lateral Peering: What ?.......................................................................................................... 2

Benefits of Multi-Lateral Peering ...............................................................................................3

Routing Flexibility .................................................................................................................. 3

Fraud Control .......................................................................................................................... 3

Centralized Accounting ..........................................................................................................3

Freedom to Scale..................................................................................................................... 4

Superior Performance ............................................................................................................. 4

Cost Effective.......................................................................................................................... 4

New Opportunities .......................................................................................................................... 4

Wholesale Traffic Exchange....................................................................................................... 4

Enterprise VoIP VPN.................................................................................................................. 5

Multi-lateral Peering with Asterisk: How? ..................................................................................... 5

Step 1: Get Asterisk .................................................................................................................... 5

Step 2: Get the OSP Toolkit........................................................................................................ 6

Step 3: Compile Asterisk with the OSP Toolkit ......................................................................... 6

Step 4: Set up an OSP Server...................................................................................................... 7

Step 5: Enrollment ...................................................................................................................... 7

Step 6 Configure Asterisk for OSP ............................................................................................. 8 extensions.conf........................................................................................................................ 8 sip.conf.................................................................................................................................... 9 osp.conf ................................................................................................................................... 9

Asterisk and Asterisk logo are trademarks of Digium, Inc.

Multi-lateral Peering: Why?

Are you …

	A carrier or a large enterprise running multiple Asterisk servers to manage VoIP traffic?

	Searching for more flexible, simple ways to manage your VoIP traffic?

	Reaching a scalability limit for maintaining IP access lists for authentication?

	Eager to benefit from the simpler, more efficient network architecture of direct peer-to- peer SIP applications?

	Struggling  with  the  cost  and  complexity  of  maintaining  growing  number  of  VoIP

interconnect billing agreements?

If your answer is “Yes” to any of the above questions, Multi-Lateral Peering is the solution to your  problems.	Multi-Lateral  Peering  –  is  a  highly  scalable  and  secure  architecture  which combines the power of the Internet with public key infrastructure (PKI) technology.  The result is secure  peer  to  peer  VoIP  networking  which  simplifies  operations,  saves  bandwidth  use  and reduces capital costs.   Multi-lateral  peering  increases profits by eliminating costs and creating new revenue opportunities.

Current Deployments

Most VoIP operators running multiple SIP gateways or SIP proxies have implemented either a distributed  or  a  centralized  architecture.	This  white  paper  compares  these  two  traditional architectural models with Multi-Lateral Peering.

Distributed Architecture

The benefits of a distributed peer to peer architecture		are	network		efficiency, quality  of  service  and  fault  tolerance. There are no network bottlenecks and no single	points	  of	   failure.		 Figure	1 illustrates		a		distributed	architecture: three  Asterisk  servers  used  as  SIP  to PSTN  gateways  are  directly  peered  to each other.   This architecture is bilateral peering.		Each  of  the  three  gateways independently  maintains  routing  plans,

IP Network

Routing Table

Billing Database

IP Access Control Lists (ACL), and Call

Detail  Records  (CDR).	Managing  this information   in   a   small   network   is   a manageable	task.	However,		as	the number	of			endpoints	increases, configuration		and		maintenance		of multiple  routing  tables,  Access  Control

Access Control List

Call Signaling

Figure 1:

Asterisk Interconnections

in a distributed architecture

Lists,  and  processing  of  CDRs  from  multiple  peers  becomes  increasingly  difficult.	In  fact, operational complexity increases by the square of the number or peers [n*(n-1)/2], making large scale peer to peer networks virtually impossible.

Centralized Architecture

The benefits of a centralized architecture are operational simplicity and control; all call control is managed by a central softswitch or session controller.

Figure  2  illustrates  the  same  network shown	in	Figure	1,	but	with	a centralized architecture that is managed by  a  central  Asterisk  server  acting  as  a softswitch. Each device is peered to the Asterisk  softswitch,  which  proxies  all

calls between peers. Centralized systems simplify	network	operations,	CDR collection, and eliminate maintenance of routing tables and Access Control Lists

Softswitch

Routing Table

configured  for  each  peer.  One  major

weakness, however, is the architecture is no  longer  a  peer  to  peer  network.   The benefits of a peer to peer SIP network – network  efficiency,  quality  of  service and   fault   tolerance   are   lost   with   a centralized architecture

	The  central  softswitch  becomes single point of failure.

Billing Database

Access Control List

Call Signaling

Figure 2:

Asterisk Interconnections

in a centralized architecture

	Routing  all  calls  through  a  central  softswitch  requires  additional  bandwidth  and  may result in lower quality of service.

	Deployment of a central softswitch is expensive.   Every call requires a dedicated voice port.  Scaling up to handle large call volumes is a challenge.

The technical solution to these problems is a new concept called Multi-Lateral Peering.

Multi-lateral Peering: What ?

Multi-lateral peering is a new VoIP architecture paradigm which leverages the best features of both distributed and centralized architectures to create a flexible and highly scalable solution for securely  managing  VoIP  traffic.   The  idea  behind  multi-lateral  peering is  to  replace  the  many bilateral  peering  relationships  in  a  distributed  architecture  with  a  single  multi-lateral  peering relationship  for  all  VoIP  peers.	The  device  which  enables  multi-lateral  peering  is  a  peering server - a single point of administrative contact for direct peering among VoIP networks.   The peering server is similar to a softswitch in the centralized model, but without the creation of a network signaling bottleneck. The peering server performs authentication, routing, inter-domain access control, and call accounting for all the endpoints within its network of peered domains,

but  it  does  so  without  interfering  in  the  call  signaling  process.  As  a  result,  the  peering  server facilitates  pure  peer-to-peer  communication  without  any  network  bottlenecks  or  bandwidth constraints. To better understand the simplicity of a multi-lateral peering architecture, refer the example network of three Asterisk servers in Figure 3.  In the middle is a peering server which is

a certificate authority.  As a trusted third party to all VoIP peers, the peering server can provide routing information and secure inter-peer access permission to peers that want to interconnect.

The  multi-lateral  peering  call  scenario in Figure 3 is described below.

1.   The  source  peer  requests  a  route from  the  peering  server  which  returns the  destination  address  and  a  digitally signed inter-peer authorization token.

2.   The source device uses the routing information  to  set  up  the  call,  peer  to peer,  to  the  destination.	The  source peer  includes  the  authorization  token in  the  SIP  INVITE  to  the  destination.

1

Peering

Server

2

Routing Table

Billing Database

The   destination   validates   the   token with   the   public   key   of   the   peering server.	If   the   token   is   valid,   the destination accepts the call.

3.   At  the  end  of  the  call,  both  the source and destination peers send Call Detail  Records  to  the  peering  server.

Access Control List

Peering Messages

Call Signaling

Figure 3:

Asterisk Interconnections

with Multi-Lateral Peering

These peering messages, also known as Usage Indication messages, are not shown in Figure 3.

Multi-lateral peering server technology is based on an open and global standard defined by the

European Telecommunications Standards Institute or ETSI (www.etsi.org).  ESTI is well known

in the telecom world as the standards body for GSM, the global technology standard for wireless phones.  The  official  name  for  the  peering  server  specification  is  ETSI  TS  101  321  or  OSP protocol for inter-domain authorization, usage reporting and pricing indication.

Benefits of Multi-Lateral Peering

Multi-lateral peering provides the benefits of both the distributed and centralized architectures without incurring the limitations inherent with either architectures.

Routing Flexibility

Multi-lateral peering using OSP offers a broad range of functionality – from a simple, light route lookup  to  a  feature  rich  peering  messages  which  convey  routing  information,  trunk  group, destination protocol, allowed usage, bandwidth, type of service and interconnect price.

Fraud Control

The peering server is also a certificate authority that establishes identities, verifies authorization, and blocks any unauthorized users. The route server acts as the trusted third party without being directly  involved  in  the  communications  path  between  the  originating  and  the  terminating networks.   It   uses   PKI   (public   key   infrastructure)   based   digitally   signed,   cryptographic authorization tokens to enforce secure access control and eliminates the need for IP access lists.

Centralized Accounting

The peering server supports centralized billing by collecting the Call Detail Records from both

the source and the destination at the end of the call. The CDRs written in an XML format defined

by the OSP standard and can easily be reformatted to the specifications of any billing system.  In addition to the ease in operations and maintenance, central collection of CDRs from both parties ensures non-repudiation and eliminates settlement disputes.

Freedom to Scale

The stateless design of multi-lateral peering gives the VoIP operator a highly scalable, reliable, and easy to maintain network architecture. By centralizing the routing, access control, and billing functionalities,  VoIP  service  providers  can  simplify  the  process  of  managing  large  scale networks.  For example, a simple configuration change which enrolls an Asterisk VoIP gateway with a peering server provides the Asterisk gateway with secure access to exchange VoIP calls with all other networks in the multi-lateral peering domain.

Superior Performance

The  architecture  is  designed  as  a  purely  distributed,  peer  to  peer  model,  which  enables developers   to   build   multi-purpose   applications   without   the   constraints   of   call   control functionality. Unlike the design of centralized architectures, this design keeps the route server

out  of  the  call  signaling  process  and  thereby  prevents  any  bottlenecks  or  bandwidth  related

Quality of Service issues. Also, since the peering server is independent from the call signaling,

the technology can work with IP communication protocol such as SIP, H.323, IAX or any other

IP application protocol.

Cost Effective

Multi-laterally peered networks are cheaper to install, operate, and maintain.  By eliminating the need  for  a  central  call  signaling  platform,  significant  capital  costs  are  eliminated.	The  IP network becomes the switch.

New Opportunities

Wholesale Traffic Exchange

Multi-lateral	peering	and	settlement provides a new business opportunity for VoIP  service  providers  to  profit  from wholesale  traffic  exchange.  No  single VoIP service provider can provide global A to Z termination services to the Public Switched  Telephone  Network  (PSTN). Low   cost,   global   termination   requires negotiating  and  managing  interconnect agreements  with  multiple  carriers  that can  provide  local  VoIP  termination  to the PSTN around the world.

Multi-lateral   peering   provides   a   very effective	mechanism	to	interconnect traffic	peer	to	peer		among	VoIP termination networks.   Wholesale traffic

$

Clearing &

Settlement

1	Peering

Server

2

$

Peering Messages

Call Signaling

Settlement

Figure 5:

Multi-Lateral Peering

Clearinghouse

exchange using multi-lateral peering is a new profit opportunity for retail VoIP service providers. Figure 5 is identical to Figure 3, except the peering server operator is acting as a clearinghouse

for  peering  traffic  -  providing  wholesale  clearing  and  settlement  services  for  traffic  exchange among  peers.	Each  peer  benefits  from  outsourcing  the  back-office  intensive  operation  of managing bilateral interconnect billing agreement.   The clearinghouse generates new profits by charging a small processing fee for providing peering and settlement services.

Enterprise VoIP VPN

Secure	multi-lateral	peering	is	well suited  for  enterprises  using  the  Internet as  a  global  wide  area  network  (WAN) among branch offices.  A central peering server   can   be   deployed   to   securely control  and  account  for  inter-office  and offnet   VoIP   calls   -   creating   virtual private VoIP network.   In Figure 4, each branch  office  manages  its  own  Asterisk PBX for intra-office or local call.   Calls between the PBXs across the VoIP VPN or   to   a   terminating   VoIP   carrier   are managed  by  centrally  operated  peering server

By  using  a  secure  peering  server,  the

Branch

Office

Branch

Office

Peering

Server

Internet

Figure 4:

VoIP VPN

Branch

Office

Branch

Office

complexity and additional bandwidth required for routing calls through a central softswitch or session border controller are eliminated. The result is a simpler, peer to peer, VoIP VPN with lower operating costs and better quality of service.

Multi-lateral Peering with Asterisk: How?

The following sections describe how to build Open Source Asterisk with the OSP Toolkit. These instructions and have been developed and tested using the following software:

Fedora Core 3 with Linux kernel version 2.6.9

Asterisk version cvs checkout -D "Oct 6 17:00:00 GMT 2005" zaptel libpri asterisk

OSP Toolkit version 3.3.4

Step 1: Get Asterisk

Obtain Asterisk V1.2

Step 1-1: Things you will need to install Asterisk™ and/or Zaptel:

ncurses, and associated -devel openssl, and associated -devel bison

Step 1-2: To be sure that you have the required packages, on Fedora, you can do the following:

rpm –q readline readline-devel openssl openssl-devel bison

Step 1-3: To check out source code from Digium’s CVS repository: Login to your Linux machine as root,

cd /usr/src

export CVSROOT=:pserver:anoncvs@cvs.digium.com:/usr/cvsroot cvs login	- the password is anoncvs

cvs checkout -r v1-2 asterisk zaptel libpri

Step 2: Get the OSP Toolkit

OSP  Toolkit  version  3.3.4  is  available  at  www.transnexus.com or  www.sipfoundry.org as  a gzipped file. Follow the following instructions to install the OSP client stack.

Step 2-1: Download the OSP Toolkit to the Linux machine, in /usr/src directory.

Step 2-2: Unzip and untar the OSP Toolkit in the /usr/src directory. The OSP Toolkit should create a directory called TK-#_#_#-YYYYMMDD where  #_#_# indicates the version and

YYYYMMDD indicates the date.

gunzip -c OSPToolkit-3.3.4.tar.gz | tar xvf -

Step 2-3: Go to src directory

cd /usr/src/TK-#_#_#-YYYYMMDD/src

Step 2-4: Edit Makefile

vi Makefile

Step 2-5: Look for a variable called INSTALL_PATH= Edit it to be INSTALL_PATH=/usr/local

Step  2-6:  Compile  OSP  Toolkit.  Check  the  compilation  logs  to  see  that  there  were  no  errors during compilation.

make clean; make install

Step 2-7: Compile enroll utility

cd /usr/src/TK-#_#_#-YYYYMMDD/enroll make clean; make linux

Step 2-8: Go to bin directory. You should see the enroll utility and the script enroll.sh.

cd /usr/src/ TK-#_#_#-YYYYMMDD/bin

Step 2-9: If the /usr/src/TK-#_#_#-YYYYMMDD/bin is not the the  PATH variable, edit

enroll.sh.

vi enroll.sh

Edit the 3 lines that begin with “enroll” to read “./enroll”.

Step 3: Compile Asterisk with the OSP Toolkit

If  Zaptel  /  Digium  cards  will  be  used  with  your  Asterisk  installation,  install  the  card  in  your machine before building Asterisk. Instructions for installing a TDM400P card are found in the

/usr/src/zaptel directory.

Step 3-1: Navigate to the Zaptel directory.

cd /usr/src/zaptel

Step 3-2: Compile Zaptel

make clean; make linux26; make install

Step 3-3: Execute the depmod command which enables the modprobe command to load Zaptel drivers.

/sbin/depmod

Step 3-4: Compile libpri

cd /usr/src/libpri

make clean; make install

Step 3-5: Compile Asterisk

cd /usr/src/asterisk

make clean; make install

If compilation is successful, you will see:

+---- Asterisk Installation Complete -------+

+	+

+ YOU MUST READ THE SECURITY DOCUMENT	+

+	+

+ Asterisk has successfully been installed. +

+ If you would like to install the sample	+

+ configuration files (overwriting any	+

+ existing config files), run:	+

+	+

+	make samples	+

+	+

+------------------ or ---------------------+

+	+

+ You can go ahead and install the Asterisk +

+ program documentation now or later run:	+

+	+

+	make progdocs	+

+	+

+ **Note** This requires that you have	+

+ doxygen installed on your local system	+

+-------------------------------------------+

Step 3-6: Install sample Asterisk configuration files. The sample files are a good reference or template for building new customized configuration files.

make samples

Your Asterisk platform is now enabled for secure, multi-lateral SIP peering.

Step 4: Set up an OSP Server

If you are setting up a live/test network, contact support@transnexus.com for a free 90 day trial

of the TransNexus commercial OSP server.

If you are experimenting, a test server is publicly available on the Internet. For access to the OSP

test	server	write	to	the	OSP	mailing	list	at	www.sipfoundry.org

(https://list.sipfoundry.org/mailman/listinfo/osp) with the IP address (public or that of outermost firewall) of your Asterisk box. Your Asterisk device, and other VoIP devices, will be added to

the test server for testing. Once your devices have been added to the OSP test server, you can proceed to enroll your device with the OSP Server (Step 5).  In addition, two open source OSP servers – RAMS and OpenOSP – are available from www.sipfoundry.org.

Step 5: Enrollment

The next step is to enable the Asterisk gateway to talk to an OSP Server. This requires Asterisk

to enroll securely with the OSP Server.

Step 5-1: Go to /usr/src/TK-#_#_#-YYYYMMDD/bin directory. You should see the utility:

enroll, and a script: enroll.sh.

cd /usr/src/TK-#_#_#-YYYYMMDD/bin/

Step 5-2: Enroll with OSP server ospserver.domain.com

./enroll.sh ospserver.domain.com or ipaddress

It will ask you for a number of inputs, you can enter random data or you can just press enter. If enrollment was successful, the last 2 lines of your log will say the following:

The certificate request was successful.

Error Code returned from localcert command : 0

You will see 4 files: cacert_0.pem, certreq.pem, localcert.pem, pkey.pem

Step 5-3: Check localcert.pem file. It will look something like this:

-----BEGIN CERTIFICATE-----

MIIBejCCASQCEQDAUTw/U3QsPxvQcSDmYgVRMA0GCSqGSIb3DQEBBAUAMDsxJTAj

BgNVBAMTHG9zcHRlc3RzZXJ2ZXIudHJhbnNuZXh1cy5jb20xEjAQBgNVBAoTCU9T

UFNlcnZlcjAeFw0wNDA4MDQyMDU1MTFaFw0wNTA4MDUyMDU1MTFaMEUxCzAJBgNV

BAYTAkFVMRMwEQYDVQQIEwpTb21lLVN0YXRlMSEwHwYDVQQKExhJbnRlcm5ldCBX

aWRnaXRzIFB0eSBMdGQwXDANBgkqhkiG9w0BAQEFAANLADBIAkEAxxRq2vuG6Lx5

93R16CTsz6FXlGELY9Ob4yj12vSVWQn5e4catRf1zGmqmY3Y/as19E/wt3PEDTVN

tEAEoVFjqQIDAQABMA0GCSqGSIb3DQEBBAUAA0EA7ACCJVeysn8dCTxtDUYnpUbt

C4DYfhr31ml5yHhn280BZaAQFzKeYo19ahzCz/lHjLXfrqVuQljnEXafpgaMlw==

-----END CERTIFICATE-----

Step 5-4: Copy the 4 files to /var/lib/asterisk/keys/

You  now  have  an  OSP  enabled  Asterisk  which  can  use  the  services  of  an  OSP  server

(ospserver.domain.com) for secure inter-domain routing, access control and CDR collection.

For more information please refer to the OSP documentation on the www.sipfoundry.org/OSP

web   site.   Also,   the   OSP   mailing   list   (https://list.sipfoundry.org/mailman/listinfo/osp)   is   a resource for technical support.

Step 6 Configure Asterisk for OSP

Asterisk  must  be  configured  to use OSP  for  multi-lateral  peering.   This section explains what parameters in the extenstion.conf, sip.conf and osp.conf files must be changed.

extensions.conf

There  are  three  applications  in  the  extensions.conf  file  for  OSP  protocol.  All  of  the  three applications take string parameters.

OSPLookup (extension [| provider [| options]])

Extension: called number

Provider: context section in osp.conf, defaults “default”

Options: j – jump to n+101 priority if the lookup was NOT successful.

OSPNext (cause)

Cause: the failure reason of the prior call

Options: j – jump to n+101 priority if the lookup was NOT successful.

OSPFinish (cause)

Cause: the failure reason of the last call

Options: j – jump to n+101 priority if the final attempt was NOT successful.

The typical dial plan for Asterisk with OSP support is as follows:

[SIPProxy]	; context name

exten => _XXXX.,1,OSPLookup(${EXTEN})	; route called number exten => _XXXX.,2,Dial(${OSPTECH}/${OSPDEST},20,tr)	; dial 1st  destination exten => _XXXX.,3,OSPNext(${DIALSTATUS})	; get 2nd  destination exten => _XXXX.,4,Dial(${OSPTECH}/${OSPDEST},20,tr)	; dial 2nd  destination exten => _XXXX.,5,OSPNext(${DIALSTATUS})	; get 3rd  destination

exten => _XXXX.,6,Dial(${OSPTECH}/${OSPDEST},20,tr)	; dial 3rd  destination exten => _XXXX.,102,Hangup	; hang up

exten => _XXXX.,104,Hangup	; hang up exten => _XXXX.,106,Hangup	; hang up

exten => h,1,OSPFinish(${DIALSTATUS})	; finish the call

sip.conf

There are two parameters for OSP protocol.

allowguest:

yes (default): allow all guest calls

no: no guest calls allowed

osp: check INVITE messages according to rules defined by ospauth

ospauth:

no (default): allow calls with other valid authentication

gateway: allow calls with valid OSP token or, if no OSP token is present, allow calls with other valid authentication.  Calls with an invalid OSP token will be blocked.

proxy: allow calls with a valid OSP token, or without an OSP token.  Calls with an invalid OSP token will be blocked.

exclusive: only allow calls with a valid OSP token

The configuration for Asterisk as a Back to Back User Agent (B2BUA) with OSP support is as follows:

[general]	; default context context=SIPProxy	; context in extensions.conf

allowguest=osp		; use OSP rules for inbound call checking ospauth=proxy	; accept calls w/ valid OSP token, or w/o OSP token realm=transnexus.com		; realm for digest authentication

bindport=5060		; UDP Port to bind to (SIP standard port is 5060) bindaddr=0.0.0.0		; IP address to bind to (0.0.0.0 binds to all) srvlookup=yes	; Enable DNS SRV lookups on outbound calls

; Note: Asterisk only uses the first host

; in SRV records

; Disabling DNS SRV lookups disables the

; ability to place SIP calls based on domain

; names to some other SIP users on the Internet

osp.conf

There are several options.

accelerate:

no (default): hardware acceleration disabled

yes: hardware acceleration enabled

tokenformat:

0 (default): signed token

1: unsigned token

2: both signed and unsigned token

privatekey: private key file

localcert: local certificate file

cacert: certificate authority key files

maxconnections: max number of simultaneous connections to the provider

retrydelay: extra delay between retries

retrylimit: max number of retries before giving up

timeout: timeout for response in milliseconds

servicepoint: OSP server address

source: local IP address

The configuration for Asterisk as a Back to Back User Agent (B2BUA) with OSP support is as follows:

[general]	; general configuration tokenformat=0	; signed token only

[default]	; provider privatekey=pkey.pem	; key files localcert=localcert.pem	; cacert=cacert_0.pem	;

maxconnections=20		; max connections retrydelay=0	; delay between tries retrylimit=2	; max retries timeout=500		; time out

servicepoint=http://osptestserver.transnexus.com:1080/osp source=[216.162.34.110]

# Text boxes

C

l

e

a

r

i

n

g

&

S

e

t

t

l

e

m

e

n

t

P

P

e

e

r

r

i

nn

g

S

e

r

v

e

r

S

e

r

e

r