VoIP Bandwidth

Calculation

VoIP Bandwidth Calculation

Executive Summary

alculating  how  much  bandwidth  a  Voice  over  IP call  occupies  can  feel  a  bit  like  trying  to  answer the  question;  “How  elastic  is  a  piece  of  string?”

However,  armed  with  a  basic  understanding  of  the  parts that  make  up  the  whole,  the  question  becomes  easier  to understand.   This  White  Paper  examines  the  process  that turns voice into Voice over IP.

Overview

The  amount  of  bandwidth  required  to  carry  voice  over  an  IP network is dependent upon a number of factors.  Among the most important are:

¯    Codec (coder/decoder) and sample period

¯    IP header

¯    Transmission medium

¯    Silence suppression

The codec determines the actual amount of bandwidth that the voice data will occupy.  It also determines the rate at which the voice is sampled.  The IP/UDP/RTP header can generally be thought of as

a fixed overhead of 40 octets per packet, though on point-to-point links RTP header compression can reduce this to 2 to 4 octets (RFC

2508).   The transmission medium, such as Ethernet, will add its own headers, checksums and spacers to the packet.  Finally, some codecs employ silence suppression, which can reduce the required bandwidth by as much as 50 percent.

The Codec

Together, these give us the size of the frame.   For example, take

a G.711 codec sampling at 20 ms.   This generates 50 frames of data per second.  G.711 transmits 64,000 bits per second so each frame will contain 64,000¸ 50 = 1,280 bits or 160 octets.

Frames and Packets

Many IP phones simply place one frame of data in each packet. However, some place more than one frame in each packet.   For example, the G.729a codec works with a 10 ms sample period and produces a very small frame (10 bytes).   It is more efficient to place two frames in each packet.   This decreases the packet transmission overhead without increasing the latency excessively.

Latency and Packet Overhead

The  choice  of  the  number  of  frames  per  packet  is  a  trade-off between two characteristics: latency and packet overhead.

Long  sample  periods  produce  high  latency,  which  can  affect the  perceived  quality  of  the  call.   Long  delays  make  interactive conversations  awkward,  with  the  two  parties  often  talking  over each  other.    Based  on  this  fact  alone,  the  shorter  the  sample period, the better the perceived quality of the call.  However, there

is a price to pay.   The shorter the sample period, the smaller the frames and the more significant the packet headers become.  For the smallest packets, well over half of the bandwidth used is taken up by the packet headers; clearly an undesirable case.  See figure

1 below:

Figure 1 - IP header forms a significant part of small Voice over IP packets

IP	UDP	RTP	Data

The conversion of the analogue waveform to a digital form is carried out  by  a  codec.	The  codec  samples  the  waveform  at  regular intervals and generates a value for each sample.  These samples are typically taken 8,000 times a second.  These individual values are accumulated for a fixed period to create a frame of data.  A sample  period  of  20  ms  is  common.   Some  codecs  use  longer

The IP Header

IP Header

(Overhead)

Voice Payload

(Useful Data)

AI0106A

sample periods, such as 30 ms employed by G.723.1.   Others use shorter periods, such as 10 ms employed by G.729a.

The important characteristics of the codec are:

¯    The number of bits produced per second

¯    The  sample  period  -  this  defines  how  often  the  samples are transmitted

The term ‘IP header’ is used to refer to the combined IP, UDP and RTP information placed in the packet.  The payload generated by the codec is wrapped in successive layers of information in order to deliver it to its destination.  These layers are:

¯    IP – Internet Protocol

¯    UDP – User Datagram Protocol

¯    RTP – Real-time Transport Protocol

RTP is the first, or innermost, layer added.  This is 12 octets.  RTP

allows  the  samples  to  be  reconstructed  in  the  correct  order  and provides a mechanism for measuring delay and jitter.

UDP adds 8 octets, and routes the data to the correct destination port.   It  is  a  connectionless  protocol  and  does  not  provide  any sequence information or guarantee of delivery.

Transmission  of  IP  over  other  mediums  will  result  in  different

overhead calculations.

Voice  over  IP  over  Ethernet,  Example  1: G.711

Example 1: G.711 codec, 1 x 20 ms sample per packet - 95,200 kbps

IP  adds  20  octets,  and  is  responsible  for  delivering  the  data  to the destination host.   It is connectionless and does not guarantee delivery  or  that  packets  will  arrive  in  the  same  order  they  were sent.

Ethernet Preamble (8)

Ethernet Header (14)

IP Header (40)

Ethernet Inter-Frame Gap (12)

Ethernet CRC (4)

20 ms G.711 Payload (160)

In total, the IP/UDP/RTP   headers add a fixed 40 octets to the payload.   With  a  sample  period  of  20  ms,  the  IP  headers  will generate an additional fixed 16 kbps to whatever codec is being used.

The  payload  for  the  G.711  codec  and  20  ms  sample  period

¯    Codec G.711 – 64 kbps, 20 ms sample period

¯    1 frames per packet (20 ms)

¯    Standard IP headers

¯    Ethernet transmission medium

AI0105A

calculated  above  is  160  octets,  the  IP  header  adds  40  octets. This  means  200  octets,  or  1,600  bits  sent  50  times  a  second

– result 80,000 bits per second.  This is the bandwidth needed to transport the Voice over IP only, it does not take into account the physical transmission medium.

There are other factors, which can reduce the overhead incurred by the IP headers, such as compressed RTP (cRTP).   This can be implemented on point-to-point links and reduces the IP header from

40 to just 2 or 4 octets.  Though this is not that common today, its

One packet is sent every 20 ms, 50 packets per second.  Payload

is 64,000 ÷ 50 = 1,280 bits (160 octets).  Fixed IP overhead 40 octets, fixed Ethernet overhead 38 octets.   Total size 238 octets. Bandwidth  required  is  (160  +  40  +  38)  x  50  x  8  =  95,200 kbps.

Voice  over  IP  over  Ethernet,  Example  2: G729a

Example 2: G.729a codec, 2 x 10 ms samples per packet - 39,200 kbps

Ethernet Preamble (8)	Ethernet CRC (4)

use will become more widespread with it being implemented with

3G mobile networks.

Ethernet Header (14)

Ethernet Inter-Frame Gap (12)

The Transmission Medium

In order to travel through the IP network, the IP packet is wrapped

IP Header (40)

20 ms G.729a Payload (20)

AI0107a

in another layer by the physical transmission medium.  Most Voice over IP transmissions will probably start their journey over Ethernet, and  parts  of  the  core  transmission  network  are  also  likely  to  be Ethernet.

Ethernet has a minimum payload size of 46 octets.   Carrying IP packets with a fixed IP header of 40 means that the codec data must be at least 6 octets – typically not a problem.  The Ethernet packet starts with an 8 octet preamble followed by a header made up of

14 octets defining the source and destination MAC addresses and the length.  The payload is followed by a 4 octet CRC.  Finally, the packets must be separated by a minimum 12 octet gap.  The result

is an additional Ethernet overhead of 38 octets.

Ethernet adds a further 38 octets to our 200 octets of G.711 codec frame and IP header.  Sent 50 times a second – result 95,200 bits per second, see example 1 below.  This is the bandwidth needed to transmit Voice over IP over Ethernet.

¯    Codec G.729a – 8 kbps, 10 ms sample period

¯    2 frames per packet (20 ms)

¯    Standard IP headers

¯    Ethernet transmission medium

One packet is sent every 20 ms, 50 packets per second.  Payload

is  8,000  ÷  50  =  160  bits  (20  octets).   Fixed  IP  overhead  40 octets, fixed Ethernet overhead 38 octets.   Total size 98 octets. Bandwidth required is (20 + 40 + 38) x 50 x 8 = 39,200 kbps.

Silence Suppression

Certain   codecs   support   silence   suppression.	Voice   Activity Detection (VAD) suppresses the transmission of data during silence periods. As only one person normally speaks at a time, this can reduce the demand for bandwidth by as much as 50 percent. The receiving codec will normally generate comfort noise during the silence periods.

Additional Codec Data

| Code c | Bandwidth | Sample | Frame | Frames/ | Ethernet |
| --- | --- | --- | --- | --- | --- |
|  |  | period | size | packet | Bandwidth |
| G.711 (PCM) | 64 kbps | 20 ms | 160 | 1 | 95.2 kbps |
| G.723.1A (ACELP) | 5.3 kbps | 30 ms | 20 | 1 | 26.1 kbps |
| G.723.1A (MP-MLQ) | 6.4 kbps | 30 ms | 24 | 1 | 27.2 kbps |
| G.726 (ADPCM) | 32 kbps | 20 ms | 80 | 1 | 63.2 kbps |
| G.728 (LD-CELP) | 16 kbps | 2.5 ms | 5 | 4 | 78.4 kbps |
| G.729A (CS-CELP) | 8 kbps | 10 ms | 10 | 2 | 39.2 kbps |
| AMR (ACELP) | 4.75 kbps | 20 ms | 12 | 1 | 36.0 kbps |
| AMR (ACELP) | 7.4 kbps | 20 ms | 19 | 1 | 38.8 kbps |
| AMR (ACELP) | 12.2 kbps | 20 ms | 31 | 1 | 43.6 kbps |
| AMR-WB/G.722.2 | 6.6 kbps | 20 ms | 17 | 1 | 38.0 kbps |
| (ACELP) |  |  |  |  |  |

Summary

Although  there  are  many  factors  that  influence  the  amount  of bandwidth  required  to  transmit  a  voice  call  over  an  IP  network, by  approaching  the  problem  one  element  at  a  time  the  final calculation becomes relatively simple.  Other factors may influence the  actual  bandwidth  used,  such  as  RTP  header  compression, silence suppression and other techniques still under development.

Glossary

ACELP	Algebraic CELP (codec)

ADPCM	Adaptive Differential Pulse Code Modulation

(codec)

AMR	Adaptive Multi-Rate (GSM2 codec)

AMR-WB	Adaptive Multi-Rate Wideband (3GPP codec

G.722.2)

CELP	Code Excited Linear Predictive (codec) Codec	Coder/Decoder

CRC	Cyclic Redundancy Code

cRTP	Compressed RTP (RFC 2508) CS-CELP	Conjugate-Structure CELP

IP	Internet Protocol

LD-CELP	Low Delay CELP (codec)

MP-MLQ	Multi-Pulse Maximum Likelihood Quantization

Octet	A sequence of 8 bits

PCM	Pulse Code Modulation (codec) RFC	Request For Comment

RTP	Real-time Transport Protocol

SB-ADPCM	Sub-Band ADPCM

UDP	User Datagram Protocol

VAD	Voice Activity Detection

www.newport-networks.com	info@newport-networks.com

The Newport Networks’ logo is a registered trademark of Newport Networks Ltd.  MediaProxy™ and SignallingProxy™ are trademarks of Newport Networks Ltd.  ©2005 Newport Networks Limited.  All rights reserved.  Whilst every effort has been made to ensure that the information included in this publication is accurate at the time of going to press, Newport Networks Ltd assumes no responsibility for the accuracy of the information.  Newport Networks Ltd reserves the right to change their specifications at any time without prior notice.  Some features described in this document may be planned for future releases and may not be available in the current product.  Newport Networks Ltd reserves the right to modify its product development schedule without notice and does not guarantee that any feature or product mentioned in this document will be produced or produced in the form described.

91-052-01-0003-C

# Text boxes

C